## Slide 2: Omaha - Groundwater Assessment to Date
Alan Pattle / Aslan Perwick
Principal Hydrogeologist / Hydrogeologist
Pattle Delamore Partners Ltd
Auckland
Omaha WWTP Consultative Group Point Wells Hall 28 Feb 2015
PATTLE DELAMORE PARTNERS LTD
solutions for your environment

## Slide 3: Starting Point - Omaha Flats
Some geology information from a number of registered bores in the area
Some groundwater information from monitoring bores

## Slide 4: Investigations Completed – Omaha Flats
Coastline survey
‘Drain’ inspections
6x auger holes
~2 km of Ground Penetrating Radar (GPR) surveys
~600 m of Electro-Magnetic (EM) surveys
4x groundwater quality samples
Completed as of Feb 2015
Inform Conceptual Model

## Slide 5: Geological Observations – Omaha Flats
Indications that peat/organic silts present at the surface across entire Omaha WWTP land area
Significant peat/organic silts present on air strip (Grice land)
Average peat/organic silt thickness ~5 m, typically varying from 2 m – 7.5 m

## Slide 6: Peat Exposure – Omaha Flats Coastline

## Slide 7: DRAFT – GPF Imagery

## Slide 8: Groundwater Assessment – Omaha Flats
Drains likely to impart significant control of shallow groundwater. Configuration and flow important aspects to consider
Drains likely to be draining groundwater nearly all year round and have altered the natural groundwater flow regime
Some groundwater from beneath irrigation area could be captured by drains.

## Slide 9: Drains at Omaha Flats

## Slide 10
Shallow – typically within 1m of ground surface
‘Fresh’ (low salinity), slightly acidic
Indications of anoxic conditions
High concentrations of DOC
Low concentrations of contaminants of interest
Groundwater at Omaha Flats

## Slide 11: Planned Works – Omaha Flats
Survey and monitor major drains in the vicinity of the Omaha WWTP
Hydraulic testing of groundwater monitoring wells on irrigation site
In-depth groundwater chemistry assessments
Update conceptual model with the new information
Update Conceptual Model

## Slide 12: Mangatawhiri Spit

## Slide 13: Mangatawhiri Spit – Starting Point
Some geology information and assumptions
Some groundwater level information

## Slide 14: Investigations Completed – Mangatawhiri Spit
Coastline and site survey
‘8x auger holes
~2 km of Ground Penetrating Radar (GPR) surveys
~2.5 km of Electro-Magnetic (EM) surveys
1x groundwater quality sample (bore)
2x groundwater quality samples (beach)
Completed as of Feb 2015
Inform Conceptual Model

## Slide 15: Geological Observations – Mangatawhiri Spit
Indications that sandy material present at the surface across the majority of the OGC irrigated area
Potentially some peat/high organic and/or clayey/silty layers or lenses, but small in comparison to the coverage of sand
Silt & sand mixtures, with appreciable organic content, dominant in top 2 m of geology west of the Kahikatea forest

## Slide 16: Hand Auger Returns – OGC

## Slide 17
Shallow beneath OGC (~1-2 m bGL)
Deeper in high elevation dune areas (>4 m bGL)
‘Fresh’ (low salinity), slightly acidic
Oxidised conditions
Low concentrations of contaminants of interest
Groundwater at Mangatawhiri Spit - OGC

## Slide 19: Planned Works – Mangatawhiri Spit
Planning and installation of additional monitoring bores
Hydraulic testing of existing and new groundwater monitoring wells
In-depth groundwater chemistry assessments
Update conceptual model with the new information
Update Conceptual Model

## Slide 20: Thank you Q & A?